## Slide 1: Challenge 1: Different server configurations
Protocols needs to be topology aware to effectively use hardware links.
GPU3
GPU0
GPU2
GPU1
GPU4
GPU7
GPU5
GPU6
DGX1-P100 (NVLink 1st Gen, ~18GB/s)
DGX1-V100 (NVLink 2nd Gen, ~23GB/s)

## Slide 2: Challenge 2: Link heterogeneity
NVLink topology
PCIe topology
GPU3
GPU0
GPU2
GPU1
GPU4
GPU7
GPU5
GPU6
GPU3
GPU0
Ring-based collectives can only utilize homogeneous links.
GPU1

## Slide 3: Challenge 2: Link heterogeneity
NVLink topology
PCIe topology
33
GPU3
GPU0
GPU2
GPU1
GPU4
GPU7
GPU5
GPU6
GPU3
GPU0
Ring-based collectives can only utilize homogeneous links.
GPU1
Why not heterogeneous links?
e.g. PCIe will be bottleneck if included in a NVLink ring

## Slide 4: Challenge 3: Fragmentation in multi-tenant clusters
Within each 8-GPU server, # of GPUs allocated to 40,000 multi-GPU jobs at Microsoft.
Examples of fragmented allocation (8GPU job across 2 servers)
3 + 5
2 + 6
34

## Slide 5: Challenge 3: Fragmentation in multi-tenant clusters
Within each 8-GPU server, # of GPUs allocated to 40,000 multi-GPU jobs at Microsoft.
Why fragmentation?
Many cluster schedulers are not topology-aware.
Without support for efficient migration, DNN jobs must embrace fragmentation to avoid queuing delays.

## Slide 6: Challenge 3: Fragmentation in multi-tenant clusters
Irregular topo.  no ring
Existing solutions (NCCL) fall back to PCIe if they cannot form a NVLink ring.
GPU3
GPU0
GPU2
GPU1
GPU4
GPU7
GPU5
GPU6
Within each 8-GPU server, # of GPUs allocated to 40,000 multi-GPU jobs at Microsoft.
Why fragmentation?
Many cluster schedulers are not topology-aware.
Without support for efficient migration, DNN jobs must embrace fragmentation to avoid queuing delays.

## Slide 7: Can we do better than state-of-the-art?
Topology Heterogeneity
Different server configurations
Link heterogeneity
Fragmentation in multi-tenant clusters
Ring-based collective communication protocols

## Slide 8: Can we do better than state-of-the-art?
BLINK
Topology Heterogeneity
Different server configurations
Link heterogeneity
Fragmentation in multi-tenant clusters

## Slide 9: Talk Outline
Motivation
Challenges to achieving high-performance collective communication
  Different server configurations
  Link heterogeneity
  Fragmentation in multi-tenant clusters
Design
Evaluation

## Slide 10: How Blink handles topology heterogeneity
Topology Heterogeneity Blink
Different server configurations Probe available links at job run time

## Slide 11: How Blink handles topology heterogeneity
Link heterogeneity
Topology Heterogeneity Blink
Different server configurations Probe available links at job run time
Concurrent data transfer over heterogenous links

## Slide 12: How Blink handles topology heterogeneity
Link heterogeneity
Fragmentation in multi-tenant clusters (irregular topology)
Topology Heterogeneity Blink
Different server configurations Probe available links at job run time
Concurrent data transfer over heterogenous links
Spanning trees (v.s. Rings) are more flexible and optimal.

## Slide 13: How Blink handles topology heterogeneity
Link heterogeneity
Fragmentation in multi-tenant clusters (irregular topology)
Topology Heterogeneity Blink
Different server configurations Probe available links at job run time
Concurrent data transfer over heterogenous links
Spanning trees (v.s. Rings) are more flexible and optimal.
More
NCCL-compatible API, seamless integration with TF, PyTorch, etc.

## Slide 14: Blink workflow

## Slide 15: Blink workflow

## Slide 16: Broadcast comparison (Trees v.s. Rings)
6-GPU topology

## Slide 17: Broadcast comparison (Trees v.s. Rings)
Broadcast from GPU3
Unused link
NCCL 2 rings

## Slide 18: Broadcast comparison (Trees v.s. Rings)
Blink 3 Spanning trees
3 Spanning trees > 2 Rings
Use All the links available  Optimal
Broadcast from GPU3

## Slide 19: TreeGen: packing max. spanning trees
Given available topology, pack max. unidirectional spanning trees.
GPU1
GPU2
GPU3
GPU1
GPU2
GPU3
Topology
GPU1
GPU1
GPU3
GPU2 GPU3 GPU2
Packing unidirectional spanning trees

## Slide 20: TreeGen: packing max. spanning trees
GPU1
GPU2
GPU3
GPU1
GPU2
GPU3
Topology
GPU1
GPU1
GPU3
GPU2 GPU3 GPU2
Packing unidirectional spanning trees
Maximize the sum of bandwidth usage among all links
Constrain: amount of BW usage should not exceed ANY link capacity when packing multiple trees
Optimization problem
Given available topology, pack max. unidirectional spanning trees.

## Slide 21: TreeGen: packing max. spanning trees
GPU1
GPU2
GPU3
GPU1
GPU2
GPU3
Topology
GPU1
GPU1
GPU3
GPU2 GPU3 GPU2
Packing unidirectional spanning trees
Optimization problem
Too many trees!
181 spanning trees for
8-GPU DGX-1V
Maximize the sum of bandwidth usage among all links
Constrain: amount of BW usage should not exceed ANY link capacity when packing multiple trees
Given available topology, pack max. unidirectional spanning trees.
Data size per-tree is too small to fully saturate link BW.

## Slide 22: TreeGen: packing max. spanning trees
Optimization problem
Approximate packing
approxi mation
Either a tree use ALL BW of a link, or not use it.
6 trees for 8GPU DGX-1V
181 trees for 8GPU DGX-1V
approximation
Given available topology, pack max. unidirectional spanning trees.

## Slide 23: TreeGen
Given available topology, pack max. unidirectional spanning trees
Direct support for one-to-many/many-to-one primitives
  e.g. Reduce, Broadcast, etc.
Reduce
Broadcast

## Slide 24: TreeGen
Given available topology, pack max. unidirectional spanning trees
Direct support for one-to-many/many-to-one primitives
  e.g. Reduce, Broadcast, etc.
Reduce
Broadcast
Extend to many-to-many primitives (e.g. AllReduce)
  Pick a root node, reduce towards root, then broadcast in reverse direction.
Reduce 
Broadcast 
AllReduce

## Slide 25: TreeGen for NVSwitch (DGX-2)

## Slide 26: TreeGen for NVSwitch (DGX-2)
NVSwitch
GPU1
GPU2
GPU3
GPU 4
With NVSwitch, the connectivity among any subset of GPUs is uniform
NCCL constructs a multi-hop ring.
4GPU Reduce (G1->G4)

## Slide 27: TreeGen for NVSwitch (DGX-2)
NVSwitch
GPU1
GPU2
GPU3
GPU 4
With NVSwitch, the connectivity among any subset of GPUs is uniform
NCCL constructs a multi-hop ring.
Hop Count
1
4GPU Reduce (G1->G4)

## Slide 28: TreeGen for NVSwitch (DGX-2)
NVSwitch
GPU1
GPU2
GPU3
GPU 4
With NVSwitch, the connectivity among any subset of GPUs is uniform
NCCL constructs a multi-hop ring.
Hop Count
2
4GPU Reduce (G1->G4)

## Slide 29: TreeGen for NVSwitch (DGX-2)
NVSwitch
GPU1
GPU2
GPU3
GPU 4
With NVSwitch, the connectivity among any subset of GPUs is uniform
NCCL constructs a multi-hop ring.
Hop Count
3
4GPU Reduce (G1->G4)

## Slide 30: TreeGen for NVSwitch (DGX-2)
NVSwitch
GPU1
GPU2
GPU3
GPU 4
With NVSwitch, the connectivity among any subset of GPUs is uniform
NCCL constructs a multi-hop ring.
Hop Count
4
4GPU Reduce (G1->G4)

## Slide 31: TreeGen for NVSwitch (DGX-2)
DGX-2 single-hop tree
NVSwitch
GPU1
Reduce
1-hop tree introduces Min. latency
GPU2
GPU3
GPU 4
4GPU Reduce
61

## Slide 32: TreeGen for NVSwitch (DGX-2)
62
DGX-2 single-hop tree
NVSwitch
GPU1
Reduce
1-hop tree introduces Min. latency
GPU2
GPU3
GPU 4
AllReduce  Reduce, Broadcast
For N GPUs,
N 1-hop trees, with each tree responsible for 1/N data.
Broadcast

## Slide 33: Blink workflow

## Slide 34: CodeGen
Translate TreeGen output (spanning trees) into real data transfer commands
CodeGen optimizations:
  Pipelining data chunks to reduce latency

## Slide 35: CodeGen
What chunk size to use?
Translate TreeGen output (spanning trees) into real data transfer commands
CodeGen optimizations:
  Pipelining data chunks to reduce latency
• Too small, cannot fully utilize BW
• Too big, high latency

## Slide 36: CodeGen
Translate TreeGen output (spanning trees) into real data transfer commands
CodeGen optimizations:
Pipelining data chunks to reduce latency
Automatic chunk size selection MIAD
(multiple-increase, additive-decrease)
What chunk size to use?
• Too small, cannot fully utilize BW
• Too big, high latency

## Slide 37: CodeGen
Translate TreeGen output (spanning trees) into real data transfer commands
CodeGen optimizations:
Pipelining data chunks to reduce latency
Automatic chunk size selection MIAD
(multiple-increase, additive-decrease)
What chunk size to use?
• Too small, cannot fully utilize BW
• Too big, high latency

## Slide 38: CodeGen
Translate TreeGen output (spanning trees) into real data transfer commands
CodeGen optimizations:
Pipelining data chunks to reduce latency
Automatic chunk size selection MIAD
(multiple-increase, additive-decrease)
What chunk size to use?
• Too small, cannot fully utilize BW
• Too big, high latency

## Slide 39: CodeGen
Translate TreeGen output (spanning trees) into real data transfer commands
CodeGen optimizations:
Pipelining data chunks to reduce latency
Automatic chunk size selection MIAD
(multiple-increase, additive-decrease)
What chunk size to use?
• Too small, cannot fully utilize BW
• Too big, high latency

## Slide 40: Blink design recap
Packing spanning trees while minimizing trees
  Single hop trees for DGX-2 (NVSwitch)
Chunking, pipelining transfers for max link utilization
  Auto chunk size selection with MIAD
GPU stream reuse for fair sharing of links
PCIe + NVLink Hybrid transfers
Support for multi-machine collectives
Drop-in NCCL replacement (load-time, no code recompile)

## Slide 41: Talk Outline
Motivation
Challenges to achieving high-performance collective communication
  Different server configurations
  Link heterogeneity
  Fragmentation in multi-tenant clusters
Design
Evaluation
AllReduce and Broadcast Microbenchmarks
End-to-end improvements
Benefits of One-Hop Trees over Rings or Double Binary trees
Rest of the extensive evaluation  refer to the paper

## Slide 42: Microbenchmarks (DGX-1V)
GPU3
GPU0
GPU2
GPU1
GPU4
GPU7
GPU5
GPU6
Topology
AllReduce

## Slide 43: Microbenchmarks (DGX-1V)
AllReduce
GPU3
GPU0
GPU2
GPU1
GPU4
GPU7
GPU5
GPU6
Topology
NCCL2 (2 rings)

## Slide 44: Microbenchmarks (DGX-1V)
GPU3
GPU0
GPU2
GPU1
GPU4
GPU7
GPU5
GPU6
Topology
NCCL2 (2 rings)
Blink (3 spanning trees)
AllReduce

## Slide 45: Microbenchmarks (DGX-1V)
AllReduce
(up to 8x speed-up, 2x geo-mean)

## Slide 46: Microbenchmarks (DGX-1V)
Broadcast (up to 6x speed-up, 2x geo-mean)
76
AllReduce (up to 8x speed-up, 2x geo-mean)

## Slide 47: End-to-end Benchmarks (DGX-1V)
Blink end-to-end Communication time reduction (ImageNet1K)
up to 87% Communication time reduction (51% avg.)

## Slide 48: End-to-end Benchmarks (DGX-1V)
Blink end-to-end training time reduction (ImageNet1K)
Blink end-to-end Communication time reduction (ImageNet1K)
up to 87% Communication time reduction (51% avg.)
up to 40% end-to-end training time reduction

## Slide 49: Microbenchmarks (DGX-2)
16 GPU AllReduce
Throughput
(up to 3.5x speed-up)
Latency
(Up to 3.32x reduction)
Biggest win in small chunk sizes because our 1-hop tree achieve min. latency.

## Slide 50: Guanhua Wang guanhua@cs.berkeley.edu
Topology heterogeneity results in link underutilization for collectives.
Blink packs spanning trees for optimal link utilization
Auto-generates one-to-all, all-to-one, all-to-all collectives
  Broadcast, AllReduce, etc.
Faster collective communication than NCCL
  Up to 6x faster Broadcast (2x geo-mean)
  Up to 8x faster AllReduce (2x geo-mean)
  Up to 7.7x (2x geo-mean) communication time reduction in E2E data-parallel training on DGX-1 machines.

## Slide 51: Back-ups

## Slide 52: TreeGen
Handle hybrid communication (e.g. PCIe & NVLink)
  Balance amount of data transfer over different link types based on link bandwidth.
  Take link type switching (i.e. disable_peer_access) latency into account.

## Slide 53: TreeGen
Multi-server transfers

## Slide 54: Multiple DGX-1s DNN Training
8-GPU job on 2 DGX-1V machines (5-3 GPU placement)
Inter-server tput (40Gb/s) < Intra-server tput (40GB/s)
Projection with 100/400 Gbps inter-server bandwidth, highlight Blink’s advantage.